TYPICAL SPECIFICATION

ELECTRONIC SOLO® G2

ULTRASONIC LEVEL SENSOR

SPECIFICATION SECTION 11245 - Chemical Feeders

SPECIFICATION SECTION 11240 - Chemical Feed Monitoring

An Ultrasonic Level Sensor shall be provided for each tank.  Ultrasonic sensor shall be of the “self-contained” type, outputting a 4-20 mA signal proportional to the tank level.  Sensor shall have a range of up to ______ ft. (meters)  (6’/2M,10'/3M or 25'/7M).   Sensor shall have a NEMA 4X PVC housing with ______ feet (20'/6M standard) of sensor cable.

Indicator shall monitor__________(1 or 2 ) channels. The remote mounted LCD indicator shall carry CE marking and shall be housed in a NEMA 4X, UL approved enclosure. All operations shall be keypad operated & menu driven in order to avoid compromising the NEMA 4X seal at anytime.  The alphanumeric LCD readout shall have backlighting for readability in low light conditions.  Power requirement shall be ______________( 110 VAC, 220 VAC or 24 VDC)

A 6 digit numerical display shall give operator the ability to monitor chemical by weight (lb or kg) or volume (gallons or liters).  A bar graph display shall read 0-100% for the net contents.  A dual mode TARE key shall allow user to enter the tare weight of the vessel or enter the net weight of the chemical depending on application needs. A diagnostics menu shall allow recalibration without the need to fill or empty the vessel.  A user adjustable filter function shall stabilize display in the event of vibration from pumps or mixers in the immediate vicinity.

Indicator shall output net weight via a 4-20mA signal and full scale output shall be user adjustable via the keypad.  Indicator shall have four adjustable set points to display low or high level conditions on the indicator.

OPTIONAL:    Set points shall activate ______ (up to four) ½ Amp dry contact relays.

Sensor shall carry a Full Five (5) Year Factory Warranty.   “Limited” Warranties shall be considered unacceptable.   Full scale accuracy shall be better than 1/2 of 1%.   Sensor shall be ultrasonic ECHO-SCALETM  Model 5___80,  and electronic SOLO® G2 digital display Model SRG2____ (1 or 2 channel), as manufactured by FORCE FLOW, 2430 Stanwell Drive, Concord, CA 94520 USA (www.forceflow.com).

Model Numbers:

INDICATOR:	SRG2-1		One Channel

SRG2-2 		Two Channel

Model Numbers:

Model		Range			Feet of Cable

SENSOR:	5280		1' - 25' (30cm - 765cm)	20'/6M Cable (Std)

5180		1' - 10' (30cm - 305cm)	10'/3M Cable (Std

5080		4”-79” (76mm-2006mm)

FORCE FLOW   1-800-893-6723

FAX: 925-686-6713    www.forceflow.com    info@forceflow.com

ULTRASONIC/SOLOG2

02/26/09