TYPICAL SPECIFICATION

WIZARD® 4000

ULTRASONIC LEVEL SENSOR

SPECIFICATION SECTION 11245 - Chemical Feeders

SPECIFICATION SECTION 11240 - Chemical Feed Monitoring

ULTRASONIC SENSOR:     An Ultrasonic Level Sensor shall be provided for each tank.  Ultrasonic sensor shall be of the “self-contained” type, outputting a 4-20 mA signal proportional to the tank level.  Sensor shall have a range of 1' to ______ ft. (meters) (See chart below).   Sensor shall have a NEMA 4X PVC housing with ______ ft. (meters) (20'/6M standard) of sensor cable.

INSTRUMENT ENCLOSURE, OUTPUTS & ALARMS:  Indicator shall carry CE marking and shall be housed in a NEMA 4X, UL approved enclosure.   Indicator shall have a 20 key digital keypad & ability to display 2 scales at a time on a backlit alphanumeric display.  If more than 2 scales are being monitored, display shall automatically scan all scales in the system.   Indicator shall have adjustable 4-20mA signals that output net weight and chemical feed rate for each scale.  Indicator shall display an alarm in any of the following conditions: Low level, high level, low feed rate, high feed rate, max daily use, min daily use, supply exhausted and load cell failure.  An alarm log shall store the most recent 10 alarm conditions with time and date of occurrence.  A quantity of ____relays  (up to 12 per indicator) shall be provided for remote alarm indication or transfer pump control.   Indicator shall be enabled with MODBUS protocol for remote RS-485 serial communications.

DISPLAY & INVENTORY CONTROL SOFTWARE:  Keypad and Menu items shall have independent password protection to prevent unauthorized operation.  Both a numerical and a bar graph display shall give operator the ability to monitor chemical by weight, volume or percent full.    Each channel shall have a user selectable, two digit scale ID number and shall display net remaining, pure chemical remaining, feed rate, daily usage, total amount used, days until empty, gross weight and tare weight.    A TANK LOAD key shall pause & project usage accumulation during chemical re-supply to maintain accurate usage data over multiple tank loads.  A data log shall store the DAILY USAGE for each of the previous 31 days.  Indicator re-calibration in the field shall be accomplished through the keypad and shall not require the use of dead weights.

Sensor shall carry a Full Five (5) Year Factory Warranty.   “Limited” warranties shall be considered unacceptable.    Full scale accuracy shall be better than ½ of 1%.   Sensor shall be ultrasonic ECHO-SCALETM  Model 5___80, and electronic WIZARD® 4000 digital display, as manufactured by FORCE FLOW, 2430 Stanwell Drive, Concord, CA 94520 USA (www.forceflow.com).

Model Numbers:

Model		Range				Feet of Cable

SENSOR:	5180		1' - 10' (30cm - 305cm)		10'/3M Cable (Std)

5280		1' - 20' (30cm - 610cm)		20'/6M Cable (Std)

INDICATOR:	4000-1		1 Channel

4000-2		2 Channel

4000-3		3-Channel

4000-4		4-Channel

File:   _WEB\SPECS\SPCULTWZ

FORCE FLOW  1-800-893-6723

FAX: 925-686-6713

ULTRASONIC/WZ

09/03/03